## Slide 1: Combinational logic circuits
Presentation on

## Slide 2: Types of combinational logic circuits
Adders
Subtractor
Half Adder
Full Adder
Half subtracror
Full subtractor

## Slide 3: Firstly we discuss about Adder
Definition of adder:
Adders are the combinational logic circuits which are used for adding two or three binary bits.
Types of Adder:
Half adder
Full adder

## Slide 4: HALF ADDER
Definition of Half adder: Half adder add two binary digits and produces two binary outputs called sum and carry.
It generates sum(s) and carry(c) as output.
Block Diagram:
Half adder

## Slide 5: Truth table
Input bits |  | output | 
A | B | sum | carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 6: K-Map for half adder

## Slide 7: Logic expressions: s=A’B+AB’
Logic Diagram:

## Slide 8: Full Adder
Full adder has three input bits A,B and additional carry-in(in)
It is used to add three bits and generate two output sum(s),carry(c)
Block diagram:
sum
Inputs outputs
carry
Full adder

## Slide 9: Truth table
Inputs bits |  |  | outputs | 
A | B | C | Sum | carry
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 10: K-map

## Slide 11: Logic Diagram

## Slide 12
Thank
you
Download ppt’s and handwritten notes
JP Web devolpers
Follow on instagram:-@jpwebdevelopers