## Slide 1: Logic Gates
Presentation on

## Slide 2: LOGIC GATE
Logic Gates is an electronic circuit the operates on one or more signals to produce standard output signals .
Logic gate are indicated by the
-Symbol
-Truth Table
-Boolean Algebra

## Slide 3: Types of logic gates

## Slide 4: AND GATE
A Circuit which performs an AND operation.
It has n input (two or more then 2)and one output.
Output the output of AND gate is high(1) when all the input are high(1).
Algebraic function of AND gate.
X=A.B
AB
A AND B

## Slide 5: TRUTH TABLE FOR AND GATE
A | B | X(A.B)
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 6: LOGIC DIAGRAM FOR AND GATE

## Slide 7: OR GATE
A Circuit which perform OR operation.
It has n input (n>=2) and one output.
Output the output of OR gate is high (1) when if one or more inputs are high.
Algebraic function of OR gate
X=A OR B
=A+B

## Slide 8: TRUTH TABLE OF OR GATE
A | B | X
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 9: LOGIC DIAGRAM OF OR OR GATE

## Slide 10: NOT GATE
NOT gate is also known as inverter.
The output of NOT gate is high, when input is low.
Algebraic function of NOT gate.
X=A’
X=NOTA
TRUTH TABLE
A | X
0 | 1
1 | 0

## Slide 11: LOGIC DIAGRAM OF NOT GATE

## Slide 12: NAND GATE
It is a combination of AND or NOT gate.
it has n input (n>=2) and one output.
Algebraic function of NAND GATE
X=(AB)’

## Slide 13: TRUTH TABLE FOR NAND GATE
A | B | AB | X
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 14: LOGIC DIAGRAM FOR NAND GATE

## Slide 15: NOR GATE
It is combination of OR and NOT gate.
It has n input(n>=2)and one output (output is high when both input and output are low.
Algebraic function NOR gate.
X=A NOR B
(A+B)’

## Slide 16: TRUTH TABLE
A | B | A+B | X
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0

## Slide 17: LOGIC DIAGRAM FOR NOR GATE

## Slide 18: XOR GATE
XOR or EX-OR gate is a special type of gate.
The exclusive-or gate is abbereviated as ex-or gate
X-OR gate.
It has n input (n>=2) and one output.
The output is high when input are not same (one of them is 0 and other one is 1).
Algebraic Function of XOR gate
X=A XOR B
X=A’B’+AB’

## Slide 19: TRUTH TABLE FOR XOR GATE
A | B | X
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 20: LOGIC DIAGRAM OF XOR GATE

## Slide 21: EX-NOR GATE
IT is logical complement of XOR gate.
It has n input(n>=2) and one output.
The output is high(1) when both inputs 0 or both 1.
Algebraic Function of exclusive NOR
X=A EX-NOR B
=A’B’+AB

## Slide 22: LOGIC DIAGRAM FOR EX-NOR

## Slide 23
Thank
you
Download ppt’s and handwritten notes
JP Web devolpers
Follow on instagram:-@jpwebdevelopers